## Slide 1: Geostationary Station-Keeping with Reinforcement Learning
Interns: Erik Magnusson, Brian Druby, Oliver Luo
Mentors: Jim Zapata, Rich Osedacz, Michelle Stephens
9 August 2021
Notes: Erik

## Slide 2: Project Objective
What:
  Discover a more efficient station-keeping policy for geostationary satellites
Why:
  Regulations require satellites to stay within a predefined area but the methods for doing so may have room for fuel-efficiency improvement
How:
  Create a 2D environment that reflects the conditions of a constrained geostationary orbit
  Use reinforcement learning to discover a more efficient maneuver policy through trial and error
Final Outputs:
  A model capable of learning a near-optimal maneuver policy
Reinforcement Learning Agent
Orbit Propagator
Environment
Action
State
State &
Reward
Notes: Erik
- Better fuel-efficiency = extended lifespan = more money

## Slide 3: Lunisolar Gravity Effect – N/S Station-keeping
The sun and moon produce gravitational forces that torque the orbit
Affects RAAN and inclination – North/South station-keeping
Modeled as Third Body Attractions
Direction of Sun/Moon
Inclination
Notes: Brian
Lunisolar Gravity Effect
The sun and moon are not in the earth’s equatorial plane
This creates an out-of-plane force that torques the orbit of a geostationary satellite: changing both the RAAN and the inclination
Using OREKIT, this can be modeled as third body attractions producing the polar plot in the lower right hand corner
  If an orbit begins with RAAN = 270, the inclination will initially decrease, reach a minimum, then increase again
  The small peaks and troughs are the result of daily solilunar effects
The total amount of delta V needed to counteract lunisolar gravity is approximately 46 m/s each year (it varies depending on the year)

## Slide 4: Solar Radiation Pressure – E/W Station-keeping
Solar radiation pressure produces a force that changes the magnitude and direction of the eccentricity vector
Creates a longitude libation that occupies part of the deadband
Modeled as a satellite with constant effective cross-sectional area ≈ 0.06 m2/kg
Notes: Brian
Solar Radiation Pressure
Electromagnetic radiation produces a force that perturbs the magnitude and direction of the eccentricity of a geostationary satellite
  It can be approximated as two deltaVs performed when the satellite-sun line is perpendicular to the satellite-earth line
The eccentricity change creates a longitudinal libation that occupies part of the E/W deadband and therefore must be controlled
The SRP was modeled assuming a satellite of constant effective cross-sectional area
As the Earth revolves around the sun, the direction of the SRP force changes, eventually canceling out by the end of the year
  This produces the year-long period depicted in the graph in the bottom right
The total delta V needed to counteract SRP is highly dependent upon the size of the deadband, the effective cross-sectional area, and the station-keeping schedule. However, it is still significantly less than N/S control.

## Slide 5: Earth’s Triaxiality – E/W Station-keeping
Earth’s non-symmetrical gravity field produces a longitudinal acceleration towards areas of high mass density (e.g. Rocky Mountains, Mt. Everest)
Over small longitude deadband it creates a near constant change in drift rate
Parameter | Value
Gravity Field | 8th Order 8th Degree
Longitude | 115.5 E
Longitude Change | -0.00199 º/day2
Notes: Brian
Photo Courtesy of NASA GRACE Mission
Earth’s Triaxiality
The non-symmetrical gravity field of Earth produces accelerations in the longitudinal direction
  The image in the top left corner visually depicts the mass distribution of the earth
  The red over areas such as the Andes Mountains and the Rocky Mountain Range show higher mass density areas
The magnitude of the acceleration is dependent upon the station longitude of the satellite, however its nearly constant within a small deadband (for this case 0.00199 degrees per day squared)
  This produces the quasi-parabolic curve shown in the figure on the bottom right
The total delta V needed to counteract Earth’s Triaxiality is approximately 2 m/s each year (it varies depending upon the station longitude)

## Slide 6: Orbit Propagator and Perturbation Modeling
Forces to be Modeled
Lunisolar Gravity
Earth’s Triaxiality
Solar Radiation Pressure
Impulsive Station-keeping Maneuvers
Information Collected
Position
Velocity
Acceleration
Mass
Notes: Brian
All three of the previously mentioned forces, as well as impulsive station-keeping maneuvers must be accurately modeled
Orekit, a low level space dynamics library, was chosen to model these forces
It provides functionality for:
  Third body attractions
  Simple and complex solar radiation effects
  Gravity models
  Event handlers to apply impulsive maneuvers
  As well as more complex maneuvers if future iterations of this project require more accuracy
It also allows easy extraction of the state information necessary to train the ML Agent including Position, Velocity, Acceleration and Mass

## Slide 7: Reinforcement Learning
PAC-MAN example:
Notes: Erik
(def) reinforcement learning: area of machine learning focused on teaching an agent to take actions in an environment using a system of positive and negative rewards (ex: autonomous vehicles, chess engines)
image sources:
https://learning.oreilly.com/library/view/python-machine-learning/9781789955750/Text/Chapter_1.xhtml#_idParaDest-22
https://towardsdatascience.com/deep-q-network-combining-deep-reinforcement-learning-a5616bcfc207

## Slide 8: Proximal Policy Optimization (PPO)
Choosing the algorithm
  Model-Free vs. Model-Based
  Policy Optimization vs. Q-Learning
  PPO
    Supports discrete and continuous action spaces
    Outperformed competing algorithms in the Lunar Lander OpenAI environment
Feature
  Actor-Critic neural network structure
    Actor: chooses actions
    Critic: evaluates actions
Notes: Erik
Released by OpenAI researchers in 2017
  Balances ease of implementation, sample efficiency, and ease of tuning
Policy gradient method
  Learns on the current policy rather than on stored values (like in Q-Learning)
  Traditionally less sample efficient because each sample group is only used to train the mode once
Reasons:
Model-free over model-based
  “allowing the agent to pursue a trial-and-error approach to learning an optimal policy rather than trying to hand shape it with limited background knowledge”
  Would be very difficult to model the distribution of states and the environment dynamics
Policy-based methods over value-based methods
  “With relatively large action and state spaces, we don’t want to store values for every State-Action combination”
  “Samples are thrown away after they are used to update the current policy”
  Better for high-dimensional action spaces or when using continuous actions
    Value-based (e.g., DQN) can be slow bc of all the Q value calculations at each step
  Automatically implements exploration/exploitation tradeoff
PPO
  To avoid updates that send the agent down an unrecoverable path, with size of the policy update is limited via loss clipping

## Slide 9: Reinforcement Learning Flow
Actor Model
Critic Model
loss
OREKIT
Obtain reward
Transform state
Take action
Calculate new state
RL Agent
Initialize state
Notes: Erik
Overall model flow:
OREKIT initializes a new orbital state for the agent (a satellite in our case)
That state is passed to our custom environment where reward calculation and state standardization occur
Reward and standardized state are passed to the neural networks of the learning agent as inputs
Loss function updates the policy’s action probabilities based on the success of the previous action
RL agent outputs an action that is passed to OREKIT to calculate an updated state

## Slide 10: Network Structures
Do nothing
West burns
North burns
East burns
Input state
Neural Network
Action Probabilities
Scalar
Input state
Neural Network
Rating of Action Taken
Actor Model
Critic Model
Notes: Erik
Actor Model:
Takes a 7 element state space as input and outputs a maneuver option by using the softmax function on the action probabilities
Mention lack of South thruster
Critic Model:
Learns if the action taken by the Actor led the environment to be in a better state or not (measured with Generalized Advantage Estimation or estimated future rewards)
Allows the Actor to compare its current policy with a new policy and adjust accordingly

## Slide 11: Key Parameters
Clipping (Epsilon) (0.1 – 0.3)
  Limits the step size from the old policy to the new policy
Batch Size (32 – 4096)
  Number of training examples passed through the neural network at once
GAE Discount Factor (Gamma) (0 – 1)
  0: approximate next-step return, 1: approximate sum of all future rewards
  For long episodes, we need gamma < 1 for tractability/convergence
Neural network structure
  Hidden layers (1 – 3)
  Nodes (32 – 512)
Learning Rate (5x10-5 to 3x10-3)
  Controls learning rate of the optimizer (Adam, in our case)
Notes: Erik
A higher clipping term allows for greater change between policies (more exploration, less exploitation)
A higher batch size should lead to more stable updates but learns slower

## Slide 12: Training Environment (OpenAI Gym)
Adapted from Lunar Lander environment from OpenAI Gym
Constraints:
  Environment limited to two dimensions
  Time is discretized
  +/- 0.05 degrees, in 2D translates to 73.6 km
Action space
  10 elements: 3 different burn durations for 3 thrusters and do nothing
State space
  7 elements: position, velocity, acceleration for both latitude and longitude and amount of fuel remaining
Notes: Oliver

## Slide 13: Approach
Initialize PPO agent
Initializes OREKIT Propagator & Environment
3. Action
1. Updated state
Propagator
PPO Agent
Environment
Reset Propagator
If State is terminal (e.g., outside of grid, out of fuel)
2. Reward & transformed state
4. Action
Episode
If State is terminal
(e.g., outside of grid, out of fuel)
Notes: Brian
Now that we understand the Propagator, the PPO agent, and the environment we can put it all together:
First the PPO agent is initialized with all the key parameters
The PPO agent will initialize the OREKIT propagator and the Environment
This will then launch an episode:
  First, the Propagator will send a state to the environment
  The environment will determine the rewards that correspond to that state and transform the state into a form the Agent can understand, then it will send both to the PPO Agent
  The PPO Agent will incorporate the rewards, then return an action to the environment that it thinks is appropriate for the given state
  The environment will then send the action back to the propagator which will incorporate the action then update the state to the next time step
  Then the loop repeats
However, what if the state that the propagator produces is out of the satellites bounds or indicates that the satellite is out of fuel
  This is called a “terminal state”
  The environment will recognize this, end the episode and reset the propagator to the initial conditions and a new episode is started
This process is then repeated hundreds of thousands of times as the agent learns more and more

## Slide 14: Integration
Multiprocessing, one process for environment and RL agent, one process for propagator
  Propagation and training agent’s neural networks take the longest amount of time
  Perform them simultaneously
Problems
  Processes have separate address spaces and don’t share variables
  Propagator and environment will be out of sync
Notes: Oliver

## Slide 15: Integration
Pipes
  Allow processes to communicate with each other by sending messages
  Allow for synchronization of propagator and environment
Notes: Oliver

## Slide 16: Run_multiprocesses()
PPO Agent is being trained on multiple environments at the same time, each one is independent of each other
  Each environment has its own propagator
  Each environment has its own training batch
All of the processes are working simultaneously

## Slide 17: Challenges encountered
Integration of OREKIT with OpenAI Gym environment
Tuning
  Slow iteration because of the computational requirements
Complexity
  State space
  Action space
  Reward structure
Notes: Oliver
- State/action spaces
  - Moved from imperfect normalization to standardized state values
  - Testing to identify optimal orbital elements
  - Testing to identify optimal maneuver option set
- Reward structure
  - Agent would exploit any local optima in the reward function

## Slide 18: Complexity Tradeoffs
This project posed a unique challenge to balance complexity and effectiveness of the algorithm
Action Space
Simple Complex
Single Duration Thrust
Continuous Duration Thrust
Three Discrete Thrust Options Per Thruster
State Space
Simple Complex
2D Position and Velocity
Mean and Osculating Orbital Elements and Derivatives
2D Position Velocity and Acceleration
Reward Structure
Simple Complex
Simple Survival Reward
Diminishing Returns for Near Boundary Position + Fuel Penalty
Notes: Brian
Mention that each thruster has 3 options
This project required balancing complexity (and the computational penalties that it entails) with the effectiveness of the algorithm
Action Space:
  The complexity of the action space ranged from a single duration thrust for each thruster (for example 5 minutes) to a continuous distribution of duration for each thruster
  A too simple action space risks the agent not having the necessary tools to survive while a too complex action space risks giving the agent unnecessary options
  Through several tests of varying complexity, we chose to use three discrete burn time lengths for each thruster
State Space:
  The complexity of the state space ranged from providing just 4 elements (X,Y position and velocity) to providing over a dozen elements of mean and osculating orbital elements and derivatives
  A too simple state space risks the agent mistaking two different states as identical, while a too complex state space would require the agent to sift through significant amounts of useless or redundant information
  Through several tests of varying complexity, we chose to use a 7 element state space of X,Y position velocity and acceleration and the remaining fuel
Reward Structure:
  The reward structure complexity ranged from a simple reward for every time-step the satellite survives to offering diminishing returns as the satellite approaches the barrier and penalizing for fuel use
  We found that diminishing returns appeared to have little effect, while a fuel penalty often resulted in the satellite choosing to never thrust
  Therefore, the simplest reward structure of a reward for each time-step survived was chosen

## Slide 19: Final outputs
Graphs
  Remaining Fuel and Days Survived vs Episodes
  Days Survived vs Episodes
Key Metric
  Longest survival time: ~52 days
  Highest 50-episode moving average: ~22 days
Video of trained model

## Slide 20: Future Outlook
The model has shown the capacity to learn life-extending maneuver strategies
  Requires many training episodes; deep RL methods are very data hungry
  Additional computational resources
Continued experimentation:
  Varying the complexity of the action space (e.g., reduce to 4 elements, switch continuous)
  Altering key model parameters
  Applying other RL algorithms
Takeaway: There is encouraging progress towards the project goal, and success may be found with simply more time and small adjustments
Notes: Erik
Parameters
  Batch size: varied this to take into account the expected lifespan of the satellite
  Discount factor: lowered the rate at which future rewards are discounted in order to accurately value longevity
  Learning rate: variable learning rate that decreases as objective function progress is made in order to avoid losing a correct learning trajectory

## Slide 21: Questions?

## Slide 22: Appendix

## Slide 23: Sources
PPO Paper: https://arxiv.org/pdf/1707.06347.pdf
PPO Implementation: https://pylessons.com/LunarLander-v2-PPO/
OREKIT Propagation: https://gitlab.orekit.org/orekit-labs/python-wrapper/-/blob/master/examples/Propagation.ipynb
Geostationary Perturbations: Handbook of Geostationary Orbits, E. M. Soop